A Protocol for Using Geophysical Methods to Detect Viking-Age Structures

Brian N. Damiata

1Cotsen Institute of Archaeology at UCLA

The Skagafjörður Archaeological Settlement Survey aims to make an accurate assessment of the first few hundred years of Viking Age settlement in northern Iceland (Figure 1).  Toward this aim, a variety of geophysical methods were evaluated to assess their effectiveness in detecting buried archaeological features of interest.  Between 2001-2009, 16 modern farms in the Langholt region of Skagafjörður were extensively surveyed using both reconnaissance and detailed geophysical methods (Table 1).  In addition, test excavations were performed to ground-truth the geophysical interpretations.

Through trial-and-error, an efficient protocol was developed to survey new farms with the goal of detecting Viking-Age features of interest that include: structures, compacted surfaces, middens, boundary walls, cemeteries and graves.  Geophysical methods used include electromagnetics (EM; measuring both apparent ground conductivity and magnetic susceptibility), D.C. resistivity and ground-penetrating radar (GPR; detecting changes in ground impedance).  Reconnaissance surveying of large sites (several to 10 acres) can be accomplished in a few days.